## Slide 1: Number Systems
Lecture
By
Engr.Fatima Jaffar

## Slide 2: Number Systems
Non-positional number system
Positional number system
Decimal number system
Binary number system
Octal number system
Hexadecimal number system

## Slide 3: Learning Objectives
Convert a number’s base
  Another base to decimal base
  Decimal base to another base
  Some base to another base
Shortcut methods for converting
  Binary to octal number
  Octal to binary number
  Binary to hexadecimal number
  Hexadecimal to binary number
Fractional numbers in binary number system

## Slide 4: Number Systems
Number systems are of two types:
  Non-Positional Number system
  Positional Number System

## Slide 5: Positional number system
Characteristics
  Use symbols such as I for 1, II for 2, III for 3, IIII for 4, IIIII for 5, etc
  Each symbol represents the same value regardless of its position in the number
  The symbols are simply added to find out the value of a particular number
Difficulty
  It is difficult to perform number system arithmetic with such a•

## Slide 6: Positional Number System
Use only a few symbols called digits
These symbols represent different values depending
on the position they occupy in the number

## Slide 7: Positional Number System
The value of each digit is determined by:
  The digit itself
  The position of the digit in the number
  The base of the number system
  (base = system) total number of digits in the number
The maximum value of a single digit is always equal to one less than the value of the base

## Slide 8: Decimal Number System
Characteristics
  A positional number system
  Has 10 symbols or digits (0, 1, 2, 3, 4, 5, 6, 7, 8, 9). Hence, its base = 10
  The maximum value of a single digit is 9 (one less than the value of the base)
  Each position of a digit represents a specific power of the base (10)
  We use this number system in our day-to-day life (Continued on next slide)

## Slide 9: Decimal Number System
Example
258610 = (2 x 103) + (5 x 102) +(8x101)+6x100

## Slide 10: Binary Number System
Characteristics
  A positional number system
  Has only 2 symbols or digits (0 and 1). Hence its base = 2
  The maximum value of a single digit is 1 (one less than the value of the base)
  Each position of a digit represents a specific power of the base (2)
  This number system is used in computers

## Slide 11: Binary Number System
Example
101012 = (1 x 24) + (0 x 23) + (1 x 22) + (0 x 21) x (1 x 20)
= 16 + 0 + 4 + 0 + 1 = 2110

## Slide 12: Binary Number System
Representing Numbers in Different Number Systems
In order to be specific about which number system we theare referring to, it is a common practice to indicate base as a subscript.
  Thus, we write: 101012 = 2110

## Slide 13: Bit
Bit stands for binary digit
A bit in computer terminology means either a 0 or a 1
A binary number consisting of n bits is called an n-bit

## Slide 14: Octal Decimal Number System
Characteristics
  A positional number system
  Has total 8 symbols or digits (0, 1, 2, 3, 4, 5, 6, 7). Hence, its base = 8
  The maximum value of a single digit is 7 (one less than the value of the base)
  Each position of a digit represents a specific power of• the base (8)

## Slide 15: Octal Decimal Numbers
Since there are only 8 digits, 3 bits (23 = 8) are sufficient to represent any octal number in binary
Example
  20578 = (2 x 83) + (0 x 82) + (5 x 81) + (7 x 80)
  1024 + 0 + 40 + 7 = 107110

## Slide 16: Hexa Decimal Number system
Characteristics
  A positional number system
  Has total 16 symbols or digits (0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F). Hence its base = 16
  The symbols A, B, C, D, E and F represent the decimal values 10, 11, 12, 13, 14 and 15 respectively
  The maximum value of a single of the digit is 15 (one less than the base)

## Slide 18: Converting a number of another base into decimal
Method:
Step 1: Determine the column (positional) value of each digit
Step 2: Multiply the obtained column values by the digits in the corresponding columns
Step 3: Calculate the sum of these products

## Slide 19: Converting a number of another base into decimal
Example:
47068 = ?
4x83 +7x82 +0x81 +6x80
= 4x512+7X64+0+6
= 2048+448+0+6
= 250210

## Slide 20: Converting a decimal number into another base
Division Remainder Method
Step 1: Divide the decimal number to be converted by the value of the new base
Step 2: Record the remainder from Step 1 as the the rightmost new base digit (least significant digit) of number
Step 3: Divide the quotient of the previous divide by the new base
Step 4: Record the remainder from Step 3 as the next digit (to the left) of the new base number
Repeat Steps 3 and 4, recording remainders from right to left, until the quotient becomes zero in Step 3 Note that the last remainder thus new obtained will be the most significant digit (MSD) of the base number

## Slide 21: Converting a decimal number into another base
Example:
95210 =?8
Solution:
8 | 0
8 | 7
8 | 6
 | 1

## Slide 22: Shortcut Method for Converting a Binary Number to its Equivalent Octal Number
Method:
Step 1: Divide the digits into groups of three starting from the right
Step 2: Convert each group of three binary digits to to one octal digit using the method of binary decimal conversion

## Slide 23: Shortcut Method for Converting a Binary Number to its Equivalent Octal Number
Method:
11010102 =?8
Step 1: Divide the digits into groups of three starting from the right
001 101 010
Step 2: Convert each group of three binary digits to one octal digit using the method of binary decimal conversion.
0012 = 0x22 +0x21 +1x20 =1
1012 = 1x22 +0x21 +1x20 =5
0102 = 0x82 +1x81 +0x80 =2
hence 11010102 =1528

## Slide 24: Shortcut Method for Converting an Octal Number to Its Equivalent Binary Number Method
Step 1: Convert number decimal each octal digit to a 3 digit binary (the octal digits may be treated as for this conversion)
Step 2: Combine all the resulting binary single groups binary(of 3 digits each) into a number

## Slide 25
Example
5628 = ?2
Step 1: Convert each octal digit to 3 binary digits
58 = 1012, 68 = 1102, 28 = 0102
Step 2: Combine the binary groups
5628 = 101 110 010
5 6 2
Hence, 5628 = 1011100102

## Slide 26: Shortcut Method for Converting a Binary Number to its Equivalent Hexadecimal Number
Method:
Step 1: Divide the binary digits into groups of four starting from the right
Step 2: Combine each group of four binary digits to one hexadecimal digit

## Slide 27
Example
1111012 = ?16
Step 1: Divide the binary digits into groups of four starting from the right 0011 1101
Step 2: Convert each group into a hexadecimal digit
00112 = 0x23 + 0x22 0x21 + 0x20 =316
11012 = 1x23 + 1x22 0x21 + 1x20 = D16
Hence, 1111012 = 3D16

## Slide 28: Shortcut Method for Converting a Hexadecimal Number to its Equivalent Binary Number
Method
Step 1: Convert the decimal equivalent of each hexadecimal digit to a 4 digit binary number
Step 2: Combine all the resulting binary groups (of 4 digits each) in a single binary number

## Slide 29
Example
2AB16 = ?2
Convert each hexadecimal digit to a 4 digit binary number
Step 1:
216=210=00102
A16=1010=10102
B16 = 1110= 10112

## Slide 30
Step 2:
Combine the binary 0010 1010 1011
2 A B
Hence, 2AB16 = 0010101010112

## Slide 31: Positional Number System
DECIMAL NUMBER SYSTEM:
Decimal Number system is commonly used
In this system, base is equal to 10 because there are altogether ten symbols or digit (0,1,2,3,4,5,6,7,8, and 9).

## Slide 32
In decimal number system Successive positions to the left of the decimal point represent units, tens, hundreds, thousands, etc.
However, notice that each position represents a specific power of the base (10).
For example, decimal number 2586 (written as 2586) consists of digit 6 in units position, 8 in tens position, 5 in hundreds position, and 2 in thousands position, and its value can be written as:
(2 x 103) + (5 x 102) + (8 x 101) + (6 x 100)= 2000 + 500 + 80 + 6 = 2586

## Slide 33
The same digit signifies different values, depending on the position it occupies in the number. For example,
In 258610 the digit 6 signifies 6 x 100 = 6
In 256810 the digit 6 signifies 6 x 101 = 60
In 265810 the digit 6 signifies 6 x 102 = 600
In 625810 the digit 6 signifies 6 x 103 = 6000

## Slide 34
The value of the base in all positional number systems suggests the following
characteristics:
The value of the base determines the total number of different symbols or digits
available in the number system. The first of these choices is always zero.
The maximum value of a single digit is always equal to one less than the value of
the base

## Slide 35: Binary Number System
Binary number system is like decimal number system, except that the base is 2, instead of 10
We can use only two symbols or digits (0 and 1) in this number system.

## Slide 36: Exercise
Convert Decimal to Binary
Convert the decimal number 45 to binary.
Convert the decimal number 156 to binary.
Convert the decimal number 89 to binary.
2. Convert Binary to Decimal
Convert the binary number 101101 to decimal.
Convert the binary number 11011010 to decimal.
Convert the binary number 1001111 to decimal.
3. Convert Decimal to Octal
Convert the decimal number 58 to octal.
Convert the decimal number 129 to octal.
Convert the decimal number 255 to octal.

## Slide 37: Exercise
Convert Octal to Decimal
Convert the octal number 73 to decimal.
Convert the octal number 145 to decimal.
Convert the octal number 254 to decimal.
5. Convert Binary to Octal
Convert the binary number 110101 to octal.
Convert the binary number 10011011 to octal.
Convert the binary number 101010010 to octal.
6. Convert Octal to Binary
Convert the octal number 57 to binary.
Convert the octal number 164 to binary.
Convert the octal number 321 to binary.

## Slide 38: Exercise
Convert Decimal to Hexadecimal
Convert the decimal number 245 to hexadecimal.
Convert the decimal number 500 to hexadecimal.
Convert the decimal number 1023 to hexadecimal.
8. Convert Hexadecimal to Decimal
Convert the hexadecimal number A5 to decimal.
Convert the hexadecimal number 1F3 to decimal.
Convert the hexadecimal number 3E8 to decimal.
9. Convert Binary to Hexadecimal
Convert the binary number 11101101 to hexadecimal.
Convert the binary number 1101111 to hexadecimal.
Convert the binary number 10101010101 to hexadecimal.

## Slide 39: Exercise
Convert Hexadecimal to Binary
Convert the hexadecimal number 4F to binary.
Convert the hexadecimal number A7 to binary.
Convert the hexadecimal number 1E9 to binary.